E5 In Brief

E5 is a Portable Headphone Amplifier, designed to improve the sound quality and volume of any Digital Audio Player such as a MP3 or MP4 Player, Mobile Phone, Laptop, or Notebook.

Main feature

●Easy to carry and use in the outdoors

●New amplifier IC, with high S/N and low distortion

●Individual power switch

●Electronic volume control

●Two sound effects: Flat and bass boost mode

●Built-in Rechargeable battery

●Mini USB charger connector

●With a built-in metal clip

E5简介

Battery and charger information

E5 is powered by a rechargeable battery. Use the USB cable to connect E5 to your computer to charge, or to the usb power adapter to charge. If the battery is completely discharged, it may take a while before the charging light on. The battery can be charged and discharged hundreds of times, but it will eventually wear out and can not be replaced.

use the USB CABLE to connect E5 to your computer to charge

★Warning: When you use the headphone, your ability to hear outside sounds may be affected. Do not use the headphone where it can endanger your safety.

Specification

●Output Power: 150mW (16Ω Loaded); 16mW (300Ω Loaded)

●Signal to Noise Ratio: ≥95dB (A weight)

●Distortion: <0.009% (10mW)

●Frequency Response: 10Hz ~ 100KHz

●Suitable Headphone Impedance: 16 Ω ~ 300 Ω

●Power Supply: Built-in rechargeable Li-ion battery

●Dimensions: 44.2mm x38mm x 12.6mm

●Weight: 30g

IMPORTANT

★Keep the device dry. Precipitation, humidity, and all types of liquids or moisture can contain minerals that will corrode electronic circuits.

★Do not modify, remanufacture, attempt to immerse or expose it to water or other liquids.

★When the device not be used for a long time, the battery need to be recharged.

Doesn't work / The work is unusual

●The E5 battery might need to be recharged.

●No sound source or sound source is distorted, please check whether the sound source is normal.

●The plug of the earphone is joined incompletely, Please reinsert and put in place.

●Please use original equipped wire, or check whether the output is direct current

List of articles in the packaging

Please check whether to receive the following articles:

| Headphone Amplifier 1 | Audio Cable 2 |
| --- | --- |
| USB Cable 1 (Can only be used to charge) | User Manual 1 |

★ warranty provision

1.Amplifier： One year free maintenance.

2. Accessories : No warranty.

FiiO Warranty for reference only, please subject to the provisions of the local Sales Agents.

Guangzhou  FiiO Electronic Technology Ltd.

Tel: 020-62679040    Fax: 020-62679042

Address: 2/F, F Building, Hougang Industrial Zone, Shigang Village, Huangshi West Road, Baiyun District, Guangzhou City, China.

www.fiio.com.cn         Postcode:  510430

Qualified certificate质量合格证 V02

DATE 生产日期: (dd-mm-yyyy)

Manufactured by Fiio Made in china