FiiO                              E6

User manual of products

Please read carefully before using the product

Introduction to the FiiO E6— Headphone Amplifier

E6-Portable headphone amplifier is specially designed for MP3/MP4/mobile phone/computer that can not get best effect of high impedance from the headset due to the low power to improve the power and sound quality.

Main function

●Small size, easy to carry

●New power amplifier circuit, high SNR, low distortion

●Adopt positive and negative power supply, satisfy with large Dynamic Signal Processing

●Electronic volume control

●Key lock function

●Built-in rechargeable lithium battery, normally work above 10 hours (This for reference only)

●Built-in three types of EQ option with different bass effect and a high level option.

●Standard MINI USB connector

●Removable transparent back splint (lean 45°), to meet different needs.

Specification and parameter:

| output power | 150mW (16Ω Loaded)；16mW (300Ω Loaded) |
| --- | --- |
| SNR | ≥95dB(A weight) |
| Distortion | ＜0.009%(10mW) |
| Frequency response | 10Hz~100KHz |
| Headset impedance | 16Ω~300Ω |
| USB power supply port | DC 5V/500mA |
| Power supply mode | Built-in rechargeable lithium battery. |
| Size | 41mmx40.2mmx9mm |
| Weight | 16g |

Instruction for using

- Volume “+”

Short press:

Volume increase gradually

Long press:

Volume increase constantly

- Volume “-“

Short press: volume decrease gradually

Long press: volume decrease constantly

- line input

- USB port

- headset output

- power switch/EQ

| Power on/off | Power on: Turn the switch to direction of ⑥ for 3 seconds or above till to the blue light shining Power off: Turn switch to derection of ⑥ for 3 seconds or above, till to the blue light extinguish |
| --- | --- |
| EQ switch | Single click the switch toward ⑥ direction then loosen, can switch to EQ |
| EQ status | LED extinguish | Straight frequency response |
|  | Red | EQ1 |
|  | Blue | EQ2 |
|  | Blue & red | Apply to LO 2v high level input |

When enter EQ, there are four cycle selections of LED working status: off, red, blue, blue &red.

- lock

- Transparent back splint: removable (lean 45° design)

- EQ indicator light

- Instruction for indicator light：when the charging Completed, the red color light is off.

| Power on | Working | Blue |
| --- | --- | --- |
|  | Working& Charging | Blue & Red |
| Power off | charging | Red |

Operation instruction for back splint and charging

Usage of back clip( easy to install and remove by hand, need not any tools.

Install                                  Remove

Install from the back onto relative position,      Push backward the hold buckle, then Press

after installing, there will be a sound that        downward the clip from the front of E6 to

shows the installation is done.                   take it off.

hold Buckle

install from the back     installation done

E6 built-in lithium battery for power supply

Use USB cable to connect computer and E6 to charge for the lithium battery. If the battery discharge completely, it need to take some times to be charged then it can work normally, the lithium battery can be used for hundreds of time, but it finally will be aging and may not be replaced.

Diagram of using USB cable to charge

Usage for audio cable

Audio Player

It will get better sound effect if use a line output signal on the sound source,

such as: FiiO L3, L5, L6.

L3 (Apple DOCK)                   L5 (SONY DOCK)     L6 (sansa DOCK)

Important Notes Before Using

Important note:

★Please keep the advice dry and away from moisture and humid environment, such as rain and any liquid or water with corrosion that will damage the advice

★Do not repair, disassemble the device yourself, and do not put it on the place with water

★When you do not use this device for a long time, please charge it regularly to ensure the battery life.

★When you are using the headphone, you will not hear the voice of outside environment, in order to ensure your safety, please avoid using the headphone in a danger environment.

★If the native machine cannot work normally or you have any questions, please visit our website (  http://www.fiio.com.cn/support/FeekBack.aspx ) to post or send email to service@fiio.com.cn

Doesn't work well or abnormal

●E6 might need to be recharged.

●If there are no sound output, or sound with noise, please check the music output devices and make sure the music files are in good condition, check if the power adapter is inserted completely or not.

●Music input is possibility of unstable connecting, please pull out and plug in again the input devices to have a try.

●Please use the original cable or suitable audio cable and to ensure the normal output.

List of items in the package (please verify)

| Headphone amplifier E6 1 pcs | Audio cable 2 pcs |
| --- | --- |
| USB cable (Just for charging use) 1 pcs | Back clip 2 pcs |
| User manual 1 pcs |  |

★ warranty provision

1.Amplifier： One year free maintenance.     2. Accessories : No warranty.

FiiO Warranty for reference only, please subject to the provisions of the local Sales Agents

Qualified Certificate 质量合格证 V00

DATE 生产日期: Guangzhou FiiO Electronic Technology Ltd. （dd-mm-yyyy） Tel: 020-62679040 Fax: 020-62679042 ddress: 2/F, F Building, Hougang Industrial Zone, Shigang Village, Huangshi West Road, Baiyun District, Guangzhou, China. Postcode：510430 http:// www.fiio.com.cn QC 检验合格 5190051

Manufactured by Fiio Made in china