FiiO                                E9

User manual of products

Please read this instruction before using the product

Introduction to the FiiO E9 – Desktop Headphone Amplifier

- Headphone output jack: Suitable for the headphone with 3.5MM

plug, compare to the output jack with 6.35mm,this jack with lower

outputrangefor 5dB under the same volume condition,to

prevent the headphone or hearingdamage due to the high

range of output

- Volume control with power switch knob: clockwiserotation,

power on, indicator light③ work, the volumeincrease gradually;

Left rotation, the volume decrease gradually, power off when

turn to the end

- Indicator light: Power on, it get red at first second,

then get blue after 2 to 3 seconds, poweroff, light off

- Headphone output jack: Suitable for headphone with 6.35 plug

- DOCK connector: Specialized dock for E7, for USB DAC output

- Stereo line input connector ( 3.5mm): External audio signal input

- Stereo sound source output connector(3.5mm): Output 0-2V range variable audio signal, can adjust the output volume by ②

- RCA line output connector: Output 2V fixed range to the audio signal

- Gain switch: High gainwhen pull it upward   , suitable for headphone with high impedance or low sensitivity;

low gain when pull it downward    , suitable for low impedance or high sensitivity headphone.

- USB connector: Use for connecting computer to the E7 on the DOCK connector

- DC Power port: input port for power supply,use original power adaptor in the package,Voltage range for the power adaptor: 100-240V~, 50/60Hz

INTRODUCTION FOR E9

Main feature and function:

●Two channel power output, suitable for both of headphone with 3.5 and 6.35mm.

●Main power amplifier use the TI corporation‘s, it with 5uVrms noise,low distortion 0.00014% THD + N; high switching rate, 1300V/uS current-feedback model IC:TPA6120

●With on/off mute function;usingsealed relays for protecting power amplifier output; using ALPS sealed low noise potentiometer

●Internal audio buffer amplification BB OPA2134: FET input, with advantages of

low noise:8nVsqrHz; low distortion 0.00008%THD; high switching rate:20V/uSand so on

●E7 special base, perfect realization USB connection with audio decoding DAC, also can to E7 charging

●With LOW ( 10dB ) /HIGH(18dB) gain choice

●Two audio output: one is the 3.5mm port of E9 (adjustable output); another one is port of RCA output (fixed/ unadjustable output)

●Built-in power converter module, high efficiency, high precision and low noise, to meet great needs of dynamic signal processing

●LED power indicator light

● With function of output priority of headphone plugging-in, the external output RCA will not work after inserting headphone

●Extensible base

*The base on the top of E9 can be changed for using a special base of iPod/iPhone , but you need to buy the base of iPod/iPhone separately

Specification:

●Output power: 1W (16Ω Loaded）；80mW（600Ω Loaded）

●Headphone Impedance Range:16Ω ～600Ω

●SNR: ≥100dB（A weight）[LINE IN]

●Distortion: <0.003%（100mW）[LINE IN]

●Frequency response: 10Hz~100KHz

● Fixed line out: 2V rms

●Adjustable out: 0-2V rms

●Power supply : DC15V1.5A

●Size: 149mm×96mm×56mm

●Weight:445g

INSTRUCTION FOR USE AND CONNECTION

connection diagram as following:

IMPORTANT NOTICE

Important:

★Please keep the advice dry and away from moisture and humid environment, such as rain and any liquid or water with corrosion that will damage the advice

★Please adjust a proper volume enjoying music, to avoid damage your hearing and audio stereo system, and please turn down the volume before plugging in the earphone, do not use earphone for a long time

★Do not repair, disassemble the device yourself, and do not put it on the place with water

★Please see to it that original power supply are required, or the high quality power supply with voltage range with 15V1.5A, without warranty when the advice be damaged by the third party using unsuitable power supply

★If there is any problem with the advice or any other question, please contact us

020-62679040

Doesn't work / The work is unusual

●When without sound output, or the sound with noise, please check audio output device and the music, if they are in good condition

●It perhaps the connector of audio input and earphone out do not contact perfectly, please pull out and then plug in again

●Please use the original or suitable audio connected line, and make sure it’s normal to the output

List of items in the package (please verify)

| E9 1 | USB cable 1 |
| --- | --- |
| Power adaptor 1 | instruction 1 |

★ warranty provision

1.Amplifier： One year free maintenance.

2. Accessories : No warranty.

FiiO Warranty for reference only, please subject to the provisions of the local Sales Agents.

Qualified Certificate v00

DATE 生产日期: （dd-mm-yyyy） Guangzhou FiiO Electronic Technology Ltd. Tel: 020-62679040 Fax: 020-62679042 Address: 2/F, F Building, Hougang Industrial Zone, Shigang Village, Huangshi West Road, Baiyun District, Guangzhou City, China. Postcode: 510430 www.fiio.com.cn QC 检验合格 5190036

Manufactured by Fiio Made in china